## Slide 1
Automated Cranial 4D Flow MRI Analysis
Carson Hoffman1, Grant Roberts1, Sara Berman3, Laura Eisenmenger2, and Oliver Wieben1,2
Departments of 1Medical Physics and 2Radiology, University of Wisconsin – Madison
3Alzheimer’s Disease Research Center, University of Wisconsin – Madison
Synopsis
Background
Results
Methods
Discussion
To develop a cranial 4D flow post-processing analysis tool that includes:
    An interactive visual interface
    Quick and robust hemodynamic analysis
References
[1] Schrauben, E. et al. JMRI 2015; 42:1458-64.
[2] Gu, T. et al. AJNR 2008; 26:743-749
[3] Johnson, KM. et al. MRM 2008; 60(6):1329-1336
4D flow MRI: acquires in-vivo time-resolved 3D velocity maps
    Allows for qualitative and quantitative analysis
    Post-processing can be time consuming
A previously-established cranial 4D flow centerline processing scheme (CPS)1 allowed:
    Repeatable quantitative analysis
    Automated segmentation
    Quick post processing times (~15 min)
    Analysis of +1000 cranial cases
Purpose: Develop a quantitative velocity tool (QVT) that improves 4D flow post-processing:
    Fully automated quantitative flow computations for all vessels (~3000 locations)
      Anatomical: vessel segmentation
      Functional: blood velocity, flow, pulsatility index, etc.
    Interactive 3D user interface
      Visualization of color-coded flow parameters
      Easy vessel selection
    Reduce memory requirements and post-processing times (~5 min)
An in-vivo study will be performed to assess CPS and QVT segmentation performances, interobserver variabilities, vessel selection, and post processing times.
Ten 4D flow brain scans were acquired on healthy volunteers.
    PC-VIPR2 acquisition: field strength = 3T; volume = 22 cm3; spatial res. = 0.69 mm2; VENC = 80 cm/s; scan time = 7 min.; retrospective cardiac gating (20 frames).
The QVT graphical interface (Figure 1) was developed in MATLAB18b (Mathworks, MA).
QVT provided improved angiograms, smoother centerlines, quick vessel selection, easy visualization, and less computer memory requirements.
Robust analysis tools with high repeatability are extremely desirable for high-volume, long-term 4D flow studies.
    Both tools showed high user repeatability with an improvement for QVT.
    Local flow measurements at selected vessel locations were small (<3%).
    Flow was conserved at vessel junctions, indicating good internal consistency.
Additional users and cases will help further investigate repeatability between tools.
Figure 3: Quantitative parameters (area, flow, velocity) color-coded on automatically-generated centerlines.
Examples of segmentation improvements are shown in Figure 5.
Number of missed vessels reduced from 16.2% to 3.8% when analyzed in QVT.
    MCA, PCA, and TS accounted for 25/26 missed vessels.
    Average variance of flow along vessel segments was similar for CPS (2.8±2.6%) and QVT (2.9±2.2%).
Flow analysis was completed in 13 locations: internal carotid arteries (ICA), basilar artery (BA), middle cerebral arteries (MCA), posterior cerebral arteries (PCA), straight sinus (SS), superior sagittal sinus (SSS), and transverse sinuses (TS).
Automated vessel segmentation methods were evaluated against a manual segmentation:
    K-means segmentation (CPS)
    Threshold-based segmentation (QVT)
Number of missed (non-selectable) vessels were counted for both tools.
Intra-observer variability of flow was calculated between two observers.
Conservation of flow at ICA, MCA, ACA and TS, SS, SSS junctions was assessed with QVT.
Figure 1: 4D flow post-processing tool with 3D interactive graphical user interface. As the user moves the cursor, the cross-sectional images and flow waveforms are updated in real-time.
Regression (Figure 4) for both segmentation methods showed high correlation (R=0.96).
Threshold-based segmentation was more accurate compared to manual segmentation (slope=0.93) than k-means segmentation (slope=0.61).
Angiogram and centerline generation times decreased from 48.6 s to 13.2 s.
Automated data loading and processing increased from 3.4 min to 6 min
Processing times (vessel selection and flow validation) decreased from 15.2 min to 5.0 min (1.17 min and 0.38 min per plane).
Memory requirements were reduced from ~6GB to ~1GB
Figure 4: Linear regression (correlation) plots of k-means-derived (CPS) segmented vessel areas and iterative threshold-based (QVT) areas versus ground-truth manual segmentation.
Figure 2: Flowchart for threshold-based segmentation. This algorithm iterates through all possible thresholds and calculates L0-norm. The norm is plotted as a function of threshold, and the point of maximum curvature is the final threshold used.
Bland-Altman analysis of flow quantification between users showed a mean difference and 95% CIs of 0.042 [-0.37, 0.45] ml/s with the QVT (Figure 6).
Bias and CIs are reduced when compared to old CPS -0.1 [-1.88,1.68] ml/s.
Internal consistency of flow was observed at vessel junctions for the QVT (Figure 7).
Figure 5: Old k-means segmentation and new threshold segmentation in transverse sinus (top) and internal carotid artery (bottom).
Magnitude
Comp. Diff.
Velocity
Binary Mask
k-means
Threshold
Threshold
k-means
Transverse Sinus
Int. Carotid Artery
Figure 6: Bland-Altman plot of inter-observer repeatability for QVT.
Figure 7: Linear regression plot of inlet and outlet flow at vessel junctions (ICA, ACA, MCA and SSS, SS, TS junctions). High correlation reflects good internal flow consistency with the QVT.
A threshold-based vessel segmentation algorithm was developed (Figure 2).
Automated calculations of blood flow parameters were completed across the vascular network and color-coded in the 3D interface (Figure 3).
Figure 8: Processing times for new and old tool with 16 GB machine.